F29DC Data Communication and Networking
Coursework

Jose Fernandes H00324200

# Question 1: Lab Reports
## Lab 1: Introduction

This exercise was very important to visualise how conection-oriented and connectionless protocols differ from each other.

The TCP protocol show to have high overhead due to starting and ending handshaking but mostly due to lost packets that need to be retransmitted. The data was sent less regularly as well since the packet need to be sent in order.

The CBR type of connection had no overhead as packets were sent regularly without any handshaking or re-transmission
 requests even when packets were dropped. The data was sent disregarding its order. For these reasons it was clear that CBR transferred more data even compared with a reliable protocol such as TCP.

The Link between node 3 and node 2 was always congested especially when both TCP and BCR packets were being transferred. This caused a considerable loss of packets when node 2 was transmitting the packets. This could be prevented if the length of the trasnmission queue was increased.
I have used the droptail type of queue which simply drops the latest packets but I found

## Lab 2: Congestion

This lab was very interesting because it completes what is currently being covered on the class. Especially that poorly configured networks will not provide reliable data transmission to all nodes.

During the first data transmission occurs without any unexpected behaviour and the TCP data transmission occurs normally and it even speeds up to a constant rate of trasnmission. The behaviour changes completely as the UDP connection is established the TCP’s rate drops dramatically. The TCP data transmission relies on data ordering and the received signal from the destination for the next ordered packet to be sent.
To worsen the situation, the node 2 queue is set to be droptail type which it “punishes” reliable transmission and it ends up blocking it from being transferred.

The first stage consists on setting up 3 data tranmissions. Two connectionless and one connection oriented. It is also possible to perceived that the problem described above persists even as time goes forward and the 3 connections are running.

The second stage consist on adding a ftp connection from 4 to 0, to the existing network. The same problem with the blue connection persists, as the packets continue to be dropped constantly.

Furthermore, it is clear that the transmission delay on node 2 is as fast interval of packet arrival because its queue stays constant when no other data transmission is being undertaken.

## Lab 3: Creating a larger wired topology

Thanks to the large set of tcl files contained in the ns2 wired examples it was possible to explore many different types of wired topologies, network protocols and how to set them up.

The first exercise consists on running the “tcp4.tcl” file that runs a network composed of 3 subnetworks connected using 3 routers. The subnetwork connected to router 8 have a start topology what can suggest that the network may serve, for example a room with 5 clients. The other subnetwork are just a simple connection directly with the its router.
The connections between the routers have a different colour, maybe signalling that they operate on the link and networking layers.
Overall this might represent a scenario of a building network where each router is on a different floor and clients 7 and 3 have their own network maybe adding a extra layer of security (an access list, for example) on more sensitive resources held in the network.

This network has similarities with the tcp4 one but is way less efficient. It has many redundant routers which is good to route high traffic and to extend the network but it only has one path between the routers. To improve this network, it is necessary create more redundant links between the routers to create a mesh and balance the load of the traffic. Currently any traffic between the end-server and the clients will create a cluttered transmission where many packets will be dropped since the router queues will overflow.

This network was one of the best in terms of topologies. In this representation nodes are an abstractions for clients or routers. It is highly distributed and it might represent a peer-to-peer service where all the nodes have the same privileges. Although this network is “meshy”, it is not the optimal mesh network since it does not have links connecting each pair of nodes in the network.

This last network is a interesting example because it looks like a non-efficient rudimentary centralised topology but it might a intentional decision. If the network was poorly designed, the solution is to have the routers connected to each other, the end server and the two clients, to avoid the scenario where one link completely fail like the very last image. If this network has an intentional design, it might mean that the clients connected to one router have different access to the end server.

## Lab 4: Run, Trace ….

In this experiment, the scenarios differ only on the data link connection-oriented protocols, everything else stays the same.
There are 4 clients and two routers connected in a specific way. The 0 and 4 will communicate in a connection oriented way, node 1 and 5 will exchange a parallel connectionless communication. Both communications will share the link between the routers.

The two connection-oriented protocols behave exactly the same in the first phase of communication. Node 0 and 4 exchange the 3-way handshake that establishes an reliable “channel”, ensuring that data is sent in a sequence, without any losses or duplications.

The first scenario runs a connection-oriented protocol called “stop-n-wait” which is very simple but not very efficient as it can be seen in theses images. The sender only sends 1 packet and then it waits for the receiver to send the acknowledgement packet back. In the worst case it can wait up to the timeout which starts counting after the data packet is sent. The efficiency can be observed both in terms of time per packet but through this image, that shows that almost the full bandwith is being wasted, apart from this single packet.

The second protocol is a better solution because when the 3-way handshake is exchange, the sender and receiver agree on a size of the window, which means that agree on the amount of packets being sent at each time. This is more efficient because it sends more packets at a time, using more of the bandwidth and not waiting a full cycle per each packet.
In the first image the link between the routers is being fully used, mostly to carry the data connection-oriented packets to the destination. Then it is also visible that the acknowledgement packets are all sent in the same sequence.

In terms of tracing files, the labs 1, 2 and 3 do not differ much from each other but the tracing of the sliding window contains extra information about the acknowledgement signals that set the window size.

## Lab 5: Dynamic Networks and XGraph

This lab was compelling because I was possible to explicitly view how dynamic routing really works, in the case of a link failure.

It was visible the differences between the distance vector (DV) and link state (LS) Protocols. In the distance vector protocol the routing packets were much smaller but the network took slightly longer to recover from the link failure since the each routing packet data refers to a single node, so the adjacent nodes need to advertise the lost link. On the contrary the link state traffic is significantly heavier because packets have a global map to all other network nodes and it reduced the data packet’s traffic bandwidth. The advantage of having global information in the packets is that it the network is faster reacting to changes on the network, as it does not need to advertise the links individually.

Another event that was clear is how the network can immediately change when a link is down. In this case the network follows the ring topology so when a link goes down, the traffic flow takes the opposite direction to reliably deliver the data using another route.

Additionally, the XGraph visualising tool was also executed to process the trace file created by the tcl file. This outputted a graph, specifying the performance of each node during the period of this scenario.

## Lab 6: Ping in NS2

This activity showed how to use a networking protocol to find out more information about the reachability and network status of a connection. The first step was to ping a known host from the local machine. The chosen server was google which has the “8.8.8.8” ip address. After running the command, the protocol was monitoring the connection by sending many packet of 64 bytes and retreiving the Round Trip Time (RTT). The RTT is important to track because it is a way to track how congested a network path is by tracking its value variation. In this example the RTT (called “time” in the terminal) was pretty low and stable, so we can extrapulate that the quality of service is good.

The tcl file also was very interesting because it is possible to visualise the packet back and forth between the nodes. Although the ping packet is a control type of protocol, its packet is a data packet type that intends test the performance of the network.
## Lab 7: RED Queue Monitor using NS2

This scenario is different from other as it has a more analytical emphasis rather than visual. Its results are descriptive on how buffer allocation, link bandwidth and speed determine how congested a network might be. There were many combinations tried and some results were very clear on what configurations not to implement.
The buffer allocation protocol used is Random Early Detection (RED) is a protocol that intends to tackle high congestion using an algorithm that discards packets if its capacity is above the min and max thresholds. If the buffer capacity is only over the min threshold the drop is a randomly dropped but if its capacity is above the max threshold the last packets are dropped from the queue. This is visible in the graph were the buffer capacity average stays bounded by the thresholds. It is this way because the algorithm executes a running average to make sure the capacity is bounded by the thresholds. This buffer allocation protocol is totally different from the Drop tail because it is very basic and only drops packet when its overflown.
Many other configurations, which included decreasing buffer capacity and increasing link transmission speed and bandwidth.

# Question 2: Topologies Report
## Start Topology
### Advantages
The star topology is one of the oldest and most used topologies in networks because it is how centralised services were first created and developed, and as a result the foundational data communication protocols were designed especially for it so it is a very reliable topology.
Another important advantage of this network is for the central node, the server which has more capabilities and privileges, to provide all the resources to the client nodes to take away the work load from the nodes and secure critical data.
Due to its structure this topology is easy to scale because the network can accommodate more nodes or connect to other star topology and form a tree topology, which is equivalent to start topology. This topology is also fault tolerant than most topologies because if a issue occurs, a client can me easily added or removed.

### Disadvantages
The advantage of this topology is also its greatest flaw because if the server node is the single point of failure. If this node fails the whole network is disconnected and all the resources that clients rely on, become immediately unavailable. In contrast with a client failure that is easy to solve, the failure of the server is a problem very difficult to recover from as the communication completely shutdown.
This issue is critical specially in case of an network attack by flooding where the server is forced to shutdown because it can not handle the volume of data. This scenario can happen easily if all nodes send too much data simultaneously for a long period of time, until its buffers are completely overflow and there is no other mechanism to manage congestion rather than shutdown the machine.
Another significant disadvantage is the cost of specialised hardware needed, such as router and switches. These devices are needed to route the traffic since there are limited amount of links connecting all nodes so these central networking devices are the single point for packet and circuit routing.
## Mesh Topologies
### Advantages
The mesh topology is the most effective network topology because of its node connectivity. The number of links grows exponentially relatively to the number of nodes which entails that there are huge number of paths between every node. This balances the load of the network traffic, following an adequate routing protocol which accounts for shortest path in terms of distance and time.
This topology is the most robust wired topology because of links’ redundancy. A link failure will not cause any significant effect on the topology because a dynamic routing protocol can easily overcome this issue. For this reason it is very difficult to take a mesh network down because only the failure of most nodes or links can cause a network failure.
Another important advantage is the peer-to-peer communication that this topology enforces. Since this is a decentralised system, all the nodes have equal capabilities and privileges and there is no central node tracking the activity of every node. So if the goal is to create a distributed network, the solution is a mesh network.

### Disadvantages
The main disadvantage is the cost which is very high due of the amount of hardware and configuration needed to create and maintain such network. If the link configuration was the advantage of this network, it is also its disadvantage because you have a huge amount of links to implement, configure and maintain every link. This is the dilemma anyone designing a network must weight on, if the links’ redundancy is worth the time and money investment.
The link’s redundancy has also an impact on the routing because more links also means more routing control packets. This overhead is very significant because it requires the correct routing protocol to not cause network congestion.

# Question 3 and 4: Routing Protocols Report
## Distance Vector Protocol

Advantages
Disadvantages

## Link State Protocol

Advantages
Disadvantages
## Comparison

### Traffic Throughput
The traffic throughput in both protocols tends to decrease and tend to a high bound, which appears to be not below the 0.9 value. However the Link State, seems to perform slightly better because it tends to a higher bound.
### Packets Dropped
The total amount of dropped packets grows exponentially in both protocols but that underlines that the dropped packet‘s rate is linear. In this case the link state performs better because its rate of droppped packets is smaller than the distance vector’s.
### Packet Delivery Ratio
The packet delivery

### Total Lost Packets

### Routing Overhead

### End-to-end Delay